## Slide 1: Dynamic management of segmented structures in 3D Slicer
Csaba Pinter, Andras Lasso, and Gabor Fichtinger
Laboratory for Percutaneous Surgery, School of Computing, Queen’s University, Kingston, ON, Canada

## Slide 2: Segmentation
Head and neck RT phantom case
Also known as contouring
Delineates structures of interest
  Manual contouring: Slice by slice
  Automatic / semi-automatic
Omnipresent in medical imaging
  Surgical/radiation therapy planning
  Intra-surgery navigation
  Volume/shape analysis
  3D printing (interventions)
  Education

## Slide 3: Various representations
  Each optimal for
    either storage (A)
    or analysis (C)
    or visualization (B,D)
  Imposed needs
    Conversion
    Simultaneous
      Visualization
      Transformation
Typical representations: A: Contours, B: Surface, C: Image, D: Ribbons

## Slide 4: Difficulty #1: Operation
Brain
Brain
Operation
  User needs to be aware of the need for conversion, and also
  How to perform it
Analysis ?
Volume
Surface area
Dose volume histogram
Dice coefficient
…
Analysis ✓
Notes: Want to perform analysis on brain.
Need to convert to image so that analysis can be done. The user needs to know this.

## Slide 5: Difficulty #2: Identity
? origin ?
(provenance)
Tumor1
Brain1
Tumor
Brain
Identity
  Need to keep track of where the structures came from and what they represent
? identity ?
Operation

## Slide 6: Difficulty #3: Validity
Identity
Validity
  No invalid data should be accessible at any time
Tumor (image)
Brain (image)
Tumor (contour)
Brain (contour)
Operation
?

## Slide 7: Difficulty #4: Coherence
Patient
Patient
Identity
Validity
Brain (image)
Tumor (contour)
Brain (contour)
Operation
Coherence
  Forming a unified whole
?
Notes: “the quality of forming a unified whole”

## Slide 8: Segmentation “object”
Patient
Patient
1 segmentation contains N segments (structures)
  Coherence ✓
Provides automatic conversions
  Operation ✓
Each segment contains multiple representations
  Identity ✓
Tumor (contour)
Tumor
Brain (contour)
Brain

## Slide 9: Master representation
“Promoted” representation
Patient
Conversions use it as source
When changed, the other representations are cleared
Tumor
image
surface
  And re-converted as needed
When saving to disk, this representation is written
Solves Validity ✓
Notes: Most commonly the representation the data was acquired or stored in the first place
The representation most genuinely contains the data

## Slide 10: Automatic conversion
Driven by a dynamic graph
  Nodes are the representations
  Edges are the converters
    Can be dynamically added
    Can define representations
  Cost metrics for edges
Automatic conversion follows cheapest path
  Happens when an absent representation is requested
Contours
Ribbon
Binary image
Surface
Fractional image
1.5
2.5
3.5
2.5
2.0
4.0
2.0

## Slide 11: Implementation
Software library SegmentationCore
  Contains all the listed features
  Uses only the VTK library
  Can be integrated in many applications
Segmentations module in SlicerRT
  Advanced conversion options
  Simultaneous real-time transformation
  Advanced visualization in 2D and 3D
  Extension of the 3D Slicer platform
A. Fedorov et al. 2012
C. Pinter et al. 2012
W. Schroeder et al. 2006
Notes: + Segment editor tool for contouring directly into a segmentation object
+ Storage capabilities to DICOM and to research file formats
+ Advanced memory management by only storing the effective extent (excluding most of the empty background)
+ Automatic opacity calculation for better 3D visualization

## Slide 12: Architecture: 36 classes (C++)
vtkMRMLLabelMapVolumeNode
vtkOrientedImageData
vtkOrientedImageDataResample
vtkSegmentationConverter
vtkSegmentationConverterRule
vtkSegmentationConverterFactory
SegmentationDisplayNode
SegmentationStorageNode
vtkClosedSurfaceToBinaryLabelmapConversionRule
...
Slicer MRML
VTK storage
VTK logic
Module and widget
Displayable managers
Converter roles
Subject hierarchy plugins
vtkMRMLSegmentationNode
vtkSegmentation
vtkSegment
N
N

## Slide 13: Example use case: MRI/US fusion for prostate HDR brachytherapy

## Slide 14
Example use case: Finding most similar RT plan in the cloud
Initialize daily adaptive RT plan from most similar one
  By geometrical similarity based on segmentation comparison
Highly parallel computations
Very large amount of data
Self-driven scripts in cloud
Andrea et al., IUPESM World Congress 2015
Scripted analysis
Local control

## Slide 15: Future work
Fractional image representation
  More efficient storage of structures
  Enables using stochastic methods
Integration into 3D Slicer core
Ontologies support
  Hierarchical organization of structures
  Standard ontologies used in clinics
Binary image
Fractional image

## Slide 16
Thank you for your attention!

## Slide 17: Appendix

## Slide 18: Segmentations user interface
Managing segments and their properties
Advanced display options
Explicit handling of representations
Convenient import/export

## Slide 20: Difficulties with conversion
Operation: User needs to know that conversion is needed, and how to perform the conversion
Identity: Relationships between converted objects need to be preserved to be able to determine their origin and identity
Validity: When a representation changes, the others need to follow, otherwise invalid data is accessible
Coherence: Structures belonging together must be converted together to contain the same data types